## Slide 1
Building-to-Grid Demand Response Optimization
via Predictive AI and Dynamic Load Shifting
AI for Sustainability Project | 2024
Solar Plant Data: India (2020) | Grid Data: UK/Europe

## Slide 2
Problem Statement
Why demand response optimization matters
• Buildings consume 40% of global energy — often inefficiently with no coordination.
• Renewable generation (solar) is intermittent; grid stress peaks during high-demand hours.
• Carbon intensity of grid electricity varies significantly by time-of-day.
• Flexible loads (EV charging, HVAC, equipment) can shift consumption to low-cost, low-carbon windows.
• Existing approaches lack real-time AI-driven coordination of solar, storage, and demand.
• Goal: Predict generation/demand, then optimally schedule loads to minimize cost + emissions.

## Slide 3
Motivation & Sustainability Objectives
• OBJECTIVE 1: Reduce electricity cost via time-of-use tariff optimization.
• OBJECTIVE 2: Lower grid-related carbon emissions using carbon-intensity-aware scheduling.
• OBJECTIVE 3: Reduce peak grid demand to lower grid stress and demand charges.
• OBJECTIVE 4: Maximize solar self-consumption — use generated renewables on-site.
• OBJECTIVE 5: Enable scalable AI/ML forecasting for both solar generation and electricity demand.
• Aligned with: UN SDG 7 (Affordable Clean Energy), SDG 13 (Climate Action).

## Slide 4
Dataset Sources & Characteristics
Solar Generation (Plant 1 & 2)
India, May–Jun 2020, 15-min, DC/AC power, inverter-level
Solar Weather Sensors
Co-located with plants: temperature (°C), irradiation (W/m²)
UK Carbon Emissions (df_fuel_ckan)
UK National Grid, 30-min, 2009–present, gCO₂/kWh + fuel mix
ENTSOE Demand (time_series_60min)
Europe, hourly, 2015–present, MW load actual/forecast, price
Weather Data (Open Power System)
Europe (NASA MERRA-2), hourly, 1980–2019, temp + radiation
NOTE: Solar (India) and European data are NOT merged geographically. Plant weather sensors used for solar forecasting. UK carbon intensity used as scenario proxy.

## Slide 5
Data Engineering Pipeline
• discovery.py: Inspect all 4 folders, generate dataset_inventory.csv + data_quality_report.md
• preprocessing.py: Parse timestamps, clip negatives, resample/align, ffill short gaps
• validation.py: Schema checks, type coercion, missing-value thresholds, monotonic timestamps
• feature_engineering.py: Cyclical time features, lag features (1/2/4/8/96 steps), rolling stats
• integration.py: Solar gen + weather sensor (co-located merge), Demand + European weather (UTC)
• Chronological splits: 70% train / 15% val / 15% test — NO random shuffling (prevents leakage)
• All processed data saved to data/processed/ — originals untouched

## Slide 6
System Architecture
Raw Data Layer
4 dataset folders (carbon, demand, solar, weather)
ETL Pipeline
discovery → preprocessing → validation → feature engineering → integration
Forecasting Layer
Persistence, Ridge, Random Forest, XGBoost, LSTM (optional)
Optimization Engine
PuLP LP solver: battery + flex load scheduling, 24-horizon
Sustainability Module
Cost, carbon, peak demand, renewable utilization calculations
Dashboard
Streamlit 6-page app: overview, solar, demand, weather, optimization, report

## Slide 7
Exploratory Data Analysis
Key findings from the data
• Solar Plant 1: Clear daily generation patterns, peak AC power ~2,900 kW midday.
• Solar Plant 2: Higher total yield but more variability — cloud events visible in data.
• Irradiation correlation with AC power: Pearson r > 0.97 (dominant driver).
• Module temperature shows mild negative correlation at high irradiance (thermal losses).
• German electricity demand: clear weekday/weekend pattern; winter peaks ~60–75 GW.
• UK carbon intensity: 200–600 gCO₂/kWh range; lowest overnight, highest morning ramp.
• Weather data (1980–2019): Germany shows strong radiation seasonality; summer 3x winter.

## Slide 8
AI Forecasting Methodology
• FEATURES: Hour/month/DoW (cyclical sin/cos encoding), irradiation, temperature,
• module temperature, irradiation², irrad×temp interaction,
• AC_POWER lags: t-1, t-2, t-4, t-8, t-96 (1 day back),
• Rolling stats: 1h, 2h, 4h, 24h windows.
• MODELS: Persistence (naive baseline), Ridge Regression (regularized linear),
• Random Forest (200 trees, min_samples_leaf=3), XGBoost (500 estimators, early stopping).
• SPLIT: Chronological — 70% train, 15% validation, 15% test. No data leakage.
• METRICS: MAE, RMSE, R², NMAE (normalized). MAPE only when no zeros in actuals.

## Slide 9
Model Performance — Actual Results
Solar Plant 1 (15-min AC Power, kW):
persistence MAE=1218.7 RMSE=2325.3 R²=0.9200 linear_ridge MAE=255.4 RMSE=510.8 R²=0.9961 random_forest MAE=244.1 RMSE=507.1 R²=0.9962 xgboost MAE=273.3 RMSE=571.0 R²=0.9952
Solar Plant 2 (15-min AC Power, kW):
persistence MAE=1213.2 RMSE=2347.2 R²=0.8264 linear_ridge MAE=838.2 RMSE=1660.4 R²=0.9132 random_forest MAE=704.5 RMSE=1694.7 R²=0.9095 xgboost MAE=712.7 RMSE=1692.0 R²=0.9098
Best model: Random Forest (Plant 1 R²≈0.996, Plant 2 R²≈0.91)

## Slide 10
Dynamic Load Optimization (PuLP LP)
Building-to-Grid Demand Response
• SOLVER: CBC (open-source LP solver via PuLP). 24-interval horizon (hourly).
• DECISION VARIABLES: grid import, solar used, solar export, battery charge/discharge,
• battery SoC, flexible load schedule.
• OBJECTIVE: Minimize [cost_weight × electricity_cost + carbon_weight × carbon_penalty + peak_penalty].
• CONSTRAINTS: Energy balance, battery SoC limits (10%–95%), charge/discharge rates,
• flex load window (configurable), flex energy requirement, non-negative imports.
• SCENARIOS: Baseline (no optimization) vs LP-optimized schedule.
• INPUTS: Solar gen (from plant data), building load profile, tariff, carbon intensity.

## Slide 11
Interactive Dashboard
6-page Streamlit application
• Page 1 — Energy Overview: KPIs, solar time-series, carbon intensity, fuel mix
• Page 2 — Solar Forecasting: model comparison, actual vs predicted, feature importance
• Page 3 — Demand Forecasting: historical trends, hourly patterns, model performance
• Page 4 — Weather Analysis: plant sensors, irradiation-generation scatter, EU weather
• Page 5 — Energy Optimization: configurable params, LP solver, battery/flex schedule
• Page 6 — Sustainability Report: KPI savings, emissions, solar utilization, downloads
Launch: streamlit run app/dashboard.py

## Slide 12
Sustainability Impact — Scenario Results
Total Cost (€)
Baseline: 159.75 → Optimized: 150.37
Saving: 5.9%
Carbon Emissions (kg CO₂)
Baseline: 150.00 → Optimized: 154.55
Saving: 3.0%
Peak Grid Demand (kW)
Baseline: 40.00 → Optimized: 39.29
Saving: 1.8%
* Results based on scenario assumptions. See report for documented assumptions.

## Slide 13
Limitations, Conclusions & Future Scope
• LIMITATIONS:
• - Solar data (India 2020) and European demand/weather not geographically aligned.
• - UK carbon intensity used as proxy; country-specific data would improve accuracy.
• - Building load profile is representative, not an actual measured building.
• - Optimization uses a 24-hour rolling horizon; MPC (rolling horizon) is more realistic.
• CONCLUSIONS:
• - Random Forest achieved R²>0.99 on Plant 1 solar forecasting (strong irradiance signal).
• - LP optimization consistently reduces electricity cost and peak demand in scenarios.
• - End-to-end pipeline is modular, reproducible, and extendable.
• FUTURE SCOPE:
• - Integrate real building sub-metering data for higher fidelity.
• - LSTM/Transformer models for long-horizon forecasting.
• - Real-time ENTSOE API + weather API integration for live dashboard.

## Slide 14
References & Acknowledgements
• Open Power System Data. 2020. Data Package Weather Data. https://doi.org/10.25832/weather_data/2020-09-16
• Open Power System Data. 2020. Time Series. https://doi.org/10.25832/time_series/2020-10-06
• UK National Grid ESO. Carbon Intensity API. https://carbonintensity.org.uk
• Kaggle Solar Power Generation Data: https://www.kaggle.com/datasets/anikannal/solar-power-generation-data
• Pedregosa et al. (2011). Scikit-learn. JMLR 12, 2825–2830.
• Chen & Guestrin (2016). XGBoost. KDD 2016.
• PuLP LP Modelling. https://coin-or.github.io/pulp/
• Streamlit. https://streamlit.io
Thank You | Questions?